## Slide 1: CV5100: Modelling, Uncertainty and Data for Engineers MODULE 2: TIME SERIES ANALYSIS, lecture 1: COMPONENTS

## Slide 2: Time series
Time series is a discrete time sequence of data points indexed in time
Essentially a discretized signal which varies as a function of time
The data is typically collected at fixed intervals, expressed as (sampling interval) or as we saw earlier (sampling frequency)
Thus, time series can be denoted as a vector:
In Fourier transform, we were looking at deterministic signals. Here we assume is a random variable, considering the uncertainty introduced by noise

## Slide 3: Time series analysis (TSA)
TSA is identifying trends, seasonality and other such patterns so that we can forecast time series and make informed decisions
Why should we care?
  Time series is everywhere around us!
  Examples?
  We just don’t care about what happened! We also want to predict what will happen next
  Will the bridge be healthy after 20 years?
  What signs of early damage can the building show?
  How much will a skyscraper foundation settle 5 years later?
If a bridge starts behaving differently today than it did last year, could you detect it before failure?
  Time series analysis lets you do that
Notes: Fatigue in bridges, sway of buildings, growth of cracks, vibration of structures,

## Slide 4: Components
Time series is written as:
Time series is decomposed as
= trend
= seasonality
= offset
= irregularities or outliers
= noise

## Slide 5: components
Trend

## Slide 6: components
Seasonality

## Slide 7: components
Offset

## Slide 8: components
Noise:
  Random fluctuations in time series, some of it is coming from random factors, others is coming from systematic issues
  Noise error! Error does contribute to noise
  We would like to remove unwanted variations
Types of noise:
  White noise: Contains all frequencies with same amplitude
  Colored noise:
    Pink noise: Amplitude of frequency reduces with increase in frequency
    Brown noise: Amplitude of frequency reduces as squared rate with increase in frequency

## Slide 9: components model
Noise:
A stationary random noise yields uncorrelated and zero-mean random variables
  meaning that noise at any is not influenced by previous observations
  Thus, White noise can be represented by using Gaussian Distribution and

## Slide 10: Time series expression
Using all these components we can thus write time series as
intercept
= rate
and are signal coefficients
is frequency of signal
is the offset starting from
Heaviside step function
is the noise

## Slide 11: Example